## Slide 1
Multi-Level Factory Navigation for Quadruped Robots
MuJoCo Physics Simulation with Real ONNX Locomotion Policy + ROS2 Navigation Stack
Hongsen Pang, Hanzhuo Zhang
Shanghai Qiongpei Technology Co., Ltd.
LingTu Autonomous Navigation System | March 2026
INOVXIO | Robotics Full-Stack

## Slide 2
Research Motivation & System Overview
Challenge
Industrial factories present unique 3D navigation challenges:
• Multi-level structures with ramps, stairs, and catwalks
• Narrow passages between heavy machinery
• Dynamic obstacles (forklifts, personnel)
• GPS-denied indoor environments
Quadruped robots can traverse terrain impassable to wheeled
platforms, but require tight integration between:
1. Locomotion control (RL policy, 50Hz)
2. Terrain perception (LiDAR + traversability)
3. Global path planning (tomography-based A*)
4. Local obstacle avoidance (terrain-aware)
Simulation Architecture
┌────────────── MuJoCo Physics ─────────────┐
│ Robot MJCF (16-DOF quadruped + arm) │
│ Factory Scene (80m×55m, 4 levels) │
│ Contact physics + PD joint control │
└─────┬────────────┬────────────┬────────┘
│ │ │
▼ ▼ ▼
Odometry PointCloud2 cmd_vel
(TF/odom) (mj_multiRay) (twist)
│ │ ▲
▼ ▼ │
┌────────────── ROS2 Navigation ───────────┐
│ SLAM (Fast-LIO2/Point-LIO) │
│ Terrain Analysis → Local Planner │
│ Global Planner (PCT A*) → Path Adapter │
│ Path Follower → cmd_vel │
└──────────────────────────────────────────┘
ONNX Policy: obs_history[1,285] → actions[1,16]
5-frame history, 50Hz inference on aarch64

## Slide 3
Multi-Level Factory Scene Design (MuJoCo MJCF)
Factory Floor Plan — 80m × 55m, Total Height 13.5m
┌─── Level RF Z=13.5m ─── Roof Platform ───────────┐
│ X=48~80, Y=40~55 | HVAC, antennas, railing │
├─── Level M2 Z= 9.0m ─── Control Room ────────────┤
│ X=48~80, Y=28~55 | Control panels, windows │
├─── Level M1 Z= 4.5m ─── Mezzanine ───────────────┤
│ X=48~80, Y=0~55 | Catwalk + bridge │
├─── Level G0 Z= 0.0m ─── Main Production ─────────┤
│ Main Hall X=0~48 | Columns, machines │
│ Warehouse X=50~80 | Racks, pallets, cylinders │
│ Platform Z=+1.5 | Elevated maintenance area │
├─── Level B1 Z=-2.5m ─── Loading Dock ────────────┤
│ X=0~60, Y=0~8 | 3 truck bays, drums │
└──────────────────────────────────────────────────┘
Vertical Connections:
Ramp R1: B1 → G0 (12.5°, 20m run, 2.5m rise)
Ramp R2: G0 → +1.5m (10.7°, 14m run)
Stairs S1-S4: G0 → M1 → M2 → RF (18 steps each)
Scene Specifications
Parameter | Value
Footprint | 80m × 55m
Levels | 5 (B1, G0, M1, M2, RF)
Total Height | 13.5m
Vertical Gain | 16.5m
Horizontal Route | ~100m
Ramp Gradients | 7° – 12.5°
Obstacle Types | Columns, machinery, conveyors, racks, drums
MuJoCo Bodies | >200
Physics Timestep | 2ms (500Hz)
Integrator | RK4
Navigation Route: B1(5,3) → R1 → G0 hall → S1 → M1 → S3 → M2 → S4 → RF(72,52)

## Slide 4
RL Locomotion Policy — ONNX Deployment on aarch64
Policy Architecture (Isaac Lab trained)
Input: obs_history [1, 285] = 57 dims × 5 frames
Output: actions [1, 16] = 12 leg joints + 4 foot joints
57-dim observation vector per frame:
gyroscope(3) | projected_gravity(3) | direction(3)
joint_position(16) | joint_velocity(16) | last_action(16)
Action transform: real = output × action_scale + standing_pose
PD control: τ = kp × (target - q) - kv × dq
Critical Bug Fixes (Sim-to-Real Gap)
Issue | Root Cause | Fix
Robot collapses immediately | History buffer init with zeros (no gravity) | Warm-up with real IMU data (5 frames)
Legs splay outward | MuJoCo ↔ Dart joint order mismatch | MJ_TO_DART index array conversion
10% max speed (should be 43%+) | kv=20 >> kp torque (damping dominates) | kp×6, kv=5 (match training)
Locomotion Performance Metrics
0.33m
Standing Height
40s+
Stable Standing
43%
Walk Speed (vx=0.5)
59%
Walk Speed (vx=1.0)
12s+
Gait Stability
Joint order mapping: MJ(4+4+4+4) ↔ Dart(3+3+3+3+4) | PD Gains: kp=[390,570,720], kv=5 | 16-DOF quadruped + 6-DOF arm

## Slide 5
Simulated LiDAR — Livox Mid-360 via mj_multiRay
Raycasting Method
MuJoCo mj_multiRay API (v3.5.0):
• 6,400 rays per scan (golden angle spiral)
• 1.5ms per scan on RDK S100P (aarch64)
• Geomgroup filtering: robot=0, env=1
• Output: PointCloud2 with XYZI fields
Livox Mid-360 Pattern (OmniPerception):
• mid360.npy: 800,000 × 2 (azimuth, elevation)
• FOV: 360° azimuth, -7° ~ +52° elevation
• 20,000 rays/frame, 40-frame cycle
• Non-repetitive scanning pattern
PCT Tomogram Generation
Point Cloud → Voxelization → Tomogram (occupancy grid)
Factory Tomogram Properties:
• Shape: (5, 2, 154, 118) [Z-slices, channels, X, Y]
• Resolution: 0.2m per cell
• Center: (15.06, 8.00)m
• Slice 0: 12,978 free cells
• 23 connected components (largest: 7,755 cells)
Stored as: factory_nova.pickle (924 KB)
factory_nova.pcd (4.7 MB, visualization)
End-to-End Perception-Planning Pipeline
MuJoCo ROS2 Navigation Stack MuJoCo
────────── ─────────────────────────────────────── ──────────
mj_multiRay → PointCloud2 → terrain_analysis → localPlanner → pathFollower → cmd_vel → ONNX Policy
│ ▲ │
└─── odometry (TF) ───────────┘ │
goal_pose → PCT A* → pct_path_adapter → way_point ───┘

## Slide 6
Navigation Results — Factory Closed-Loop Tests
Quantitative Results
Test Scene | Start | Goal | Final Position | Time | Replans | Error | Result
Simple (flat) | (0, 0) | (5.0, 3.0) | (4.84, 2.89) | 10s | 0 | <0.2m | PASS
Building (25m×18m) | (2, 2) | (22, 12) | (21.85, 11.89) | 30s | 0 | <0.2m | PASS
Factory G0 (ele_planner) | (5, 3) | (14, 3, 0.35) | Goal Reached | 175s | 1 | - | PASS
Factory G0 (thru walls) | (5, 3) | (22, 10, 0.35) | Goal Reached | 301s | 6 | - | PASS
Factory G0 (Mid-360) | (5, 3) | (14, 3, 0.35) | Goal Reached | 196s | - | - | PASS
Global Plan (Python A*) | (2, 2) | (18, 9) | (21.8, 11.9) | 80s | 1 | ~4m | PASS
Key Findings
✓ All 6/6 navigation tests reached goal successfully
✓ C++ ele_planner.so works on factory_nova tomogram
✓ Python A* fallback: 7/8 goals <10ms planning time
✓ Stuck detection + auto-replan recovers from deadlocks
✓ Livox Mid-360 scan pattern improves terrain coverage
✗ Goal overshoot ~4m on long paths (arrival radius tuning)
✗ Replan-triggered waypoint reset causes temporary stalls
Global Planner Comparison
Metric | C++ ele_planner.so | Python A*
Planning Time | <5ms | <10ms
Success Rate | Requires numpy 1.x | No .so dependency
Obstacle Threshold | 50 (configurable) | 49.9 (fixed)
Path Quality | QoS: TRANSIENT_LOCAL | QoS: TRANSIENT_LOCAL
ABI Issues | numpy version conflict | None

## Slide 7
ROS2 Node Integration Tests — 8/8 PASS
ALL PASS
Test | Nodes Under Test | Checks | Duration | Status
T1 terrain_analysis | terrainAnalysis | terrain_map output, ground/obstacle intensity | 12s | PASS
T2 localPlanner | terrainAnalysis + localPlanner | Path generation, wall avoidance, stop signal | 18s | PASS
T3 pathFollower | pathFollower | cmd_vel direction, stuck detection | 15s | PASS
T4 global_planner | pct_planner_astar | Global path output, path quality | 8s | PASS
T5 pct_path_adapter | pct_path_adapter | Waypoint progression, goal_reached event | 10s | PASS
T6 full_chain | All 6 nodes | goal → cmd_vel, 5/5 checks, 18s | 18s | PASS
T7 safety_signals | localPlanner + pathFollower | E-stop, slow_down, cmd_vel zeroing | 20s | PASS
T8 han_dog_bridge | han_dog_bridge + mock/real CMS | gRPC Walk(), watchdog, joint stream | 12s | PASS
Platform: RDK S100P (aarch64) | ROS2 Humble | Real C++ nodes (terrain_analysis, localPlanner, pathFollower) + Python (global_planner, adapter)

## Slide 8
SLAM Vibration Robustness — Quadruped Gait Dataset
Dataset: Leg-KILO Corridor
Platform: Unitree Go1 quadruped robot
LiDAR: Velodyne VLP-16 (16-line, 10Hz)
IMU: Internal (~500Hz)
Scene: Indoor corridor (L-shape + return)
Duration: 445 seconds (7.4 minutes)
Messages: 670,538 total
• PointCloud2: 4,421
• IMU: 222,039
Vibration: Gait impact + body pitch oscillation
Results Summary
Scenario | Algorithm | Data Source | Result | Key Metric
Quadruped vibration | Point-LIO | Leg-KILO VLP-16 | PASS | 445s stable, loop closure
Quadruped vibration | Fast-LIO2 | Leg-KILO VLP-16 | N/A | No PointCloud2 support
Static real-time | Point-LIO | Livox Mid-360 | PASS | 0.006m drift
Static real-time | Fast-LIO2 | Livox Mid-360 | PASS | 0.008m drift
Point-LIO Trajectory Analysis (Leg-KILO Corridor, 445s)
Metric | Value
Total Distance | ~220m (110m out + 110m return)
Max Displacement | 109.9m from start
Loop Closure Error | 7.1m (no explicit loop closure)
Z-axis Drift | <1m peak (-0.88m), acceptable
IMU Init Time | <1 second (1% → 63% → 100%)
Output Rate | 10Hz stable throughout
220m
Total Trajectory
<1m
Z-drift (peak)
10Hz
Stable Output

## Slide 9
Semantic Navigation — Natural Language Goal Resolution
Fast-Slow Dual Process Architecture
System 1 (Fast Path): <200ms, rule-based
• Scene graph keyword + spatial matching
• Confidence fusion: label 35% + CLIP 35%
• Threshold: 0.75 (fused score)
• Target: >70% hit rate
System 2 (Slow Path): ~2s, LLM reasoning
• ESCA selective grounding (92.5% token reduction)
• Multi-backend: Kimi / Qwen / Claude / OpenAI
AdaNav Entropy Trigger:
entropy > 1.5 && confidence < 0.85 → force Slow Path
E2E Test Results (Factory Scene)
Instruction | Path | Time | Result
"导航到工厂大门" | Fast | 10.9s | PASS
"导航到机械设备" | Fast | 71.6s | PASS
"导航到目标区域" | Fast | 107s | PASS
Fast path confidence: 0.95 (score=0.92, well above 0.75)
Full pipeline: instruction → scene graph → goal_pose →
global_planner → adapter → local_planner → cmd_vel
Tested on factory scene with 10+ semantic objects
Mission Arc FSM — Task Lifecycle Management (New)
State Machine: IDLE → PLANNING → EXECUTING → COMPLETE
│ │
└─ RECOVERING → REPLANNING ─┘
│
FAILED (terminal)
Features: • Pure observer (subscribes to /nav/adapter_status + /nav/planner_status)
• Publishes /nav/mission_status (JSON) at 2Hz
• Integrated into gRPC TelemetryService (SlowState.navigation.mission)
• Event emission on state transitions (EventBuffer)
• 7/7 integration tests PASS

## Slide 10
Conclusion & Future Work
Contributions
1. End-to-end MuJoCo simulation framework for
quadruped navigation in multi-level industrial
environments (80m×55m, 4 levels, 13.5m height)
2. Real ONNX locomotion policy deployment on
aarch64 (RDK S100P), resolving 3 critical
sim-to-real transfer bugs
3. Full ROS2 navigation stack integration:
8/8 node-level tests + 6/6 navigation trials PASS
4. SLAM vibration robustness verified on real
quadruped gait dataset (Leg-KILO, 220m, 445s)
5. Semantic VLN with Fast-Slow dual process:
3/3 Chinese instructions resolved in <107s
Future Work
• Real-robot deployment on NOVA Thunder
quadruped (pending motor chain verification)
• Multi-floor navigation with stair traversal
(ramp G0→M1 validated, stairs pending RL policy)
• Dynamic obstacle handling with semantic
perception (YOLO-World + ConceptGraphs)
• OTA update system for field deployment
(v3.1.0 ready, Ed25519 signed manifests)
• Fleet management with gRPC telemetry
(MissionArc FSM + EventBuffer integrated)
6/6
Nav Tests PASS
8/8
Integration PASS
3/3
Semantic PASS
220m
SLAM Trajectory
16-DOF
RL Policy